## Slide 1
NETWORK SLICING IN 5G AND 6G
Creating Multiple Virtual Networks on a Single Physical Infrastructure
Subject: Computer Networks
Group ID: 8
Group Members :
Roll No. | Name
13 | Rohit Gaware
22 | Om Suryawanshi
25 | Krishna Bachkar
43 | Prathamesh Desai
Notes: Introduce the topic: network slicing lets one physical 5G network behave like many separate virtual networks. Then introduce the group.

## Slide 2: What is Network Slicing?
02
Slice 1 · Video streaming
Slice 2 · Self-driving cars
Slice 3 · IoT sensors
One shared physical network
One physical network
many virtual networks
Independent virtual slices
Own bandwidth, latency, reliability
Shared resources, less waste
Notes: A network slice is a logical, end-to-end virtual network. Each slice is tuned for one kind of service but all of them run on the same radios, links and servers.

## Slide 3: Why Do We Need Network Slicing?
03
High speed
4K video streaming
Ultra-low latency
Real-time control
High reliability
Critical services
Massive IoT
Millions of devices
Isolation
Services kept apart
Example
Autonomous vehicle
needs fast, reliable response
Smart home device
needs low data, many links
Same network,
different slices
Notes: Different applications want very different things from a network. One-size-fits-all networks cannot serve all of them well at once, which is why slicing was introduced.

## Slide 4: How Network Slicing Works
04
1
Service request
2
Identify requirements
3
Select or create slice
4
Allocate resources
5
Manage traffic
6
Monitor & optimize
Main components
Physical infrastructure
Virtual network functions
Orchestration
Monitoring
Notes: Walk through the six steps left to right. Underneath, four building blocks make it possible: physical hardware, virtual network functions, an orchestrator and monitoring.

## Slide 5: Network Slicing Architecture
05
Network slice layer
eMBB
URLLC
mMTC
Virtualization layer
Virtual compute
Virtual storage
Virtual network
Physical infrastructure
Base stations
Servers
Routers & links
Management & orchestration
Create
Configure
Monitor
Notes: Four layers: physical hardware at the bottom, a virtualization layer that carves it up, the slice layer on top, and a management and orchestration plane that controls all of them.

## Slide 6: Types of Network Slices in 5G
06
eMBB
Enhanced Mobile Broadband
Speed & capacity
4K/8K video
Cloud gaming
VR
URLLC
Ultra-Reliable Low-Latency
Fast & dependable
Automation
Control
Critical
mMTC
Massive Machine-Type
Huge device count
Smart city
Smart meters
IoT sensors
Notes: 5G defines three service categories. eMBB for speed, URLLC for latency and reliability, mMTC for connecting very large numbers of devices. Each one maps naturally to a slice type.

## Slide 7: What Each Slice Needs
07
Chart: 
| Data rate | Low latency | Reliability | Device density
eMBB | 5 | 3 | 3 | 2
URLLC | 3 | 5 | 5 | 2
mMTC | 1 | 2 | 3 | 5
eMBB
Needs the highest data rate
URLLC
Needs lowest delay and top reliability
mMTC
Needs the most connected devices
Illustrative relative scale (5 = highest need)
Notes: This radar chart is a qualitative illustration, not measured data: each slice type peaks on a different requirement, which is exactly why one shared network cannot be tuned for all of them at once.

## Slide 8: Network Slicing in 5G: End to End
08
Devices
RAN
Transport
Core
Applications
eMBB slice
URLLC slice
mMTC slice
Same infrastructure, isolated slices
Notes: Each colored pipe is one slice running from the device through the radio network, transport and core to the application. All three share the same physical nodes but stay logically separate.

## Slide 9: Network Slicing in 6G
09
AI-driven slicing
Satellite & aerial
Extended reality
Digital twins
Connected robotics
Intelligent transport
Terrestrial network
Anticipated capabilities; 6G standards are still evolving
Notes: 6G is expected to add AI-driven slice creation, tighter integration of satellite and terrestrial networks, and support for XR, digital twins and robotics. These are anticipated capabilities, not final standards.

## Slide 10: 5G vs 6G Network Slicing
10
Feature | 5G slicing | Expected 6G slicing
Management | Policy-based automation | AI-driven automation
Resources | Flexible, service-oriented | Adaptive, predictive
Coverage | Terrestrial networks | Terrestrial + non-terrestrial
Applications | IoT, streaming, industry | XR, digital twins, robotics
Optimization | Policy-based, automated | Real-time, intelligent
Status | Commercially deployed | Research & standardization
6G column shows expected capabilities
Notes: 5G slicing is deployed today and driven by policies and automation. 6G is expected to make it more intelligent and predictive, and extend it to satellites and aerial networks.

## Slide 11: Advantages of Network Slicing
11
Flexibility
Customized virtual networks
Efficiency
Shared physical infrastructure
Scalability
Adapts to changing demand
Performance
Per-service speed and latency
Isolation
Traffic managed independently
Cost-effective
No separate network per service
Notes: Six main benefits. The key ones to stress: sharing infrastructure saves cost, while isolation lets each service keep its own performance guarantees.

## Slide 12: Challenges & Security
12
Challenges
Security measures
Complex orchestration
Authentication & access control
Fair resource sharing
Traffic isolation
Keeping slices isolated
Threat monitoring
SLA monitoring
Encryption
High operational cost
Regular updates & testing
Notes: Slicing adds complexity and new attack surfaces, mainly because resources are shared. The right-hand side lists the standard measures that keep slices safe and isolated.

## Slide 13: Real-World Applications
13
Smart healthcare
Remote monitoring
URLLC
Smart manufacturing
Connected robots
URLLC
Autonomous vehicles
Connected transport
URLLC
Smart cities
Sensors & cameras
mMTC
Immersive apps
Gaming, VR and AR
eMBB
Tag = typical slice type
Notes: Each application matches one of the three slice types. The tag shows which slice would typically serve it. Future 6G may enable more advanced immersive experiences.

## Slide 14: Future Scope of Network Slicing
14
5G today
6G era
AI-based orchestration
Predictive traffic management
Autonomous optimization
Satellite & aerial integration
Energy & compute efficiency
New customized services
Notes: Future direction: networks that manage their own slices using AI, predict traffic, include satellites and aerial nodes, and use energy and compute more efficiently.

## Slide 15: Conclusion
15
One network, many slices
eMBB, URLLC and mMTC serve different needs
Security and isolation remain key
6G adds AI-driven, adaptive slicing
KEY TAKEAWAY
One physical network delivers many customized virtual networks
Notes: Summarize: slicing lets a single physical network serve very different applications. 5G made it practical; 6G is expected to make it more intelligent and adaptive.

## Slide 16
THANK YOU
Questions?
eMBB
URLLC
mMTC
Notes: Invite questions.